## Slide 1: Benefits & advantages of CoolGaN™ in high power and medium power switched mode power supplies (SMPS)
Dr. Sam Abdel-Rahman – Sr. Principal System Architect
Tamara Nenita Fallosch – Sr. Manager Product Marketing
Gökhan Sen - System Application Engineer
April 2025
Notes: Slide for Moderator

## Slide 2: Speakers
Dr. Sam Abdel-Rahman
Sr. Principal System Architect
Tamara Nenita Fallosch
Sr. Manager Product Marketing
Gökhan Sen
System Application Engineer
Notes: Slide for Moderator

## Slide 3: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42
Notes: Slide for Moderator

## Slide 4: Agenda
SMPS application description and trends
1
4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 5: AC/DC SMPS block diagram
Isolator
PFC controller
HV DC/DC
PFC
85 - 265 VAC
12 V ... 48 V
Sync rectifiers
+ ORing
Gate driver IC
Gate driver IC
Gate driver IC
Flyback controller
DC/DC controller
Aux. SMPS
Isolation
This block diagram shows power stages and topologies of SMPS

## Slide 6: CoolGaN™ in PFC and DC/DC topologies
CCM totem pole
Interleaved TCM totem pole
Legacy (past)
Mainstream (today)
In development (future)
ƞ= ~99%
Low system cost
2x CoolGaN™ Transistor 650 V G5
2x CoolMOS™ CM8 600 V
ƞ= ~98.5%
Higher system cost
1x CoolMOS™ 600 V
1x CoolSiC™ diode
4x CoolMOS™ 600 V
ƞ= ~98%
Low system cost
2x CoolMOS™ 600 V
2x CoolSiC™ diode
Classic boost w/ Active bridge
H4 bridge
ƞ= ~99.2%
Low system cost
4x CoolGaN™ Transistor 650 V G5
2x CoolMOS™ CM8 600 V
LLC
ƞ= ~97.5%
Quasi resonant
ZVS lost at light load
4x CoolGaN™ Transistor 650 V G5
OptiMOS™ / CoolGaN™ 60 – 200 V
ZVS PSFB
ƞ= ~98.5%
Full resonant  less EMI
Full soft switching  highest efficiency
Half/Full Bridge / Interleaved  scalable
CoolGaN™ Transistor 650 V G5
CoolGaN™/ OptiMOS™ 40 – 80 V
3-phase LLC
High frequency LLC fsw > 300kHz
ƞ= ~98.5%
Higher power
Natural current sharing
CoolGaN™ Transistor 650 V G5
CoolGaN™/ OptiMOS™ 40 - 80 V
ƞ= ~98.5%
Highest density
CoolGaN™ Transistor 650 V G5
CoolGaN™ Transistor 40 - 80 V G3
PFC
DC-DC
GaN
GaN
GaN
Si
GaN
Si
Si
GaN
GaN
Si
Si
Si
GaN
GaN
Si
GaN
CoolGaN™ offers efficiency up to 99% in today and next generation topologies

## Slide 7: SMPS applications trends and GaN value
Trend
Description
Power, density, efficiency
GaN values
Totem-pole PFC higher efficiency enabled by CoolGaN™
LLC high frequency and density enabled by CoolGaN™
In telecom, CoolGaN™ enables natural convection cooling SMPS (fan less)
In industrial chargers, CoolGaN™ reduces power losses caused by increased power rating
Server SMPS reaching 5.5, 8 and 12 kW, with densities > 100 W/in³
Telecom SMPS reaching 5 – 6 kW in thin form factor (height typ. 22 - 27 mm)
BBU power and density reaching up to 25 kW > 300 W/in3
Industrial chargers increase charging rate beyond 3C doubling SMPS power and density
Titanium efficiency standard 96%

## Slide 8: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 9: CoolGaN™ in current & next generation enterprise AI server with M-CRPS SMPS
Full-bridge LLC Fres = 100 - 500 kHz
CoolGaNTM Transistors 650 V G5
IGT65R035D2
IGT65R055D2
CoolGaNTM Transistors 650 V G5
IGOT65R025D2
IGLT65R017D2
CoolGaNTM Transistors 80 V G3
IGC019S08S1
IGC025S08S1
Interleaved totem-pole PFC 2 x 70 kHz
Hold-up time extension
50 V
400 V
230 VAC
3 kW CRPS PSU (3+3 redundancy)
Source: OCP Global Summit, October 2024
3 - 3.2 kW / 12 V
73 x 40 x 185 mm
~100 W/inch3 & 96% efficiency
CoolGaNTM Transistors in PFC and LLC
Current generation PSU
3.6 - 4 kW / 12 V
73 x 40 x 185 mm
>120 W/inch3 & 96% efficiency
CoolGaNTM Transistors in PFC and LLC
Next generation PSU
GaN
650 V
650 V
GaN
PSU
80 V
GaN
CoolGaN™ enables power density >120 W/in3 and efficiency >96% in next generation power supplies

## Slide 10: CoolGaN™ in next generation hyperscale AI server SMPS
Full-bridge LLC
CoolGaNTM BDS
650 V G5
IGOT65R025B2
400 V
430V
430V
2x
2x
480 VAC L-L
CoolGaNTM Transistors
650 V G5
IGOT65R025D2
IGLT65R017D2
CoolGaNTM Transistors
650 V G5
IGOT65R035D2
IGLT65R017D2
Vienna PFC
2x CoolSiCTM FET
Replaced by
1x CoolGaNTM BDS
Source: OCP Global Summit 2024 - Microsoft
Bidirectional CoolGaNTM replaces 2 x 650 V SiC in 3-ph Vienna PFC
CoolGaNTM
for soft-switching / high frequency LLC
HVDC (400 V bus voltage) requires CoolGaN™ Transistors 650 V G5 SR switches
Next generation server rack:
3-phase input
HVDC 400 V output
Up to 1 MW
GaN
BDS
650 V
650 V
650 V
GaN
GaN

## Slide 11: AI demands PSU with higher peak power and transient dynamics
ORv3-HPR
50ms | 400μs
136% | 160%
GPU draws high peak power and high load transient  LLC stage must deliver
Higher LLC switching frequency is needed to increase the control loop bandwidth
Load for AC/DC AI power
190% Load
100% Load
10% Load
130% Load
160% Load
500 μs
5 ms
50 ms
1000 ms
500 μs
500 μs
2.5 A/μs
Peak power specs according to GPU spec
CoolGaNTM along with PSoC™ C3 P8 MCU enable highest switching frequency up to 1 MHz

## Slide 12: CoolGaN™ in next generation server BBU (battery back-up unit)
BBU
Battery
Battery managements system
DC/DC converter
State of art solutions for 48 V bus architecture |  | 
Topology | Multiphase buck or boost | Multiphase buck boost
Limited to | <44 VBAT_MAX | <60 VBAT_MAX
 | <4.4 kW | >4.4 kW to <12 kW
xN
xN
Increasing power density
Chart: Volume [in^3]
| 3.3 | 4.4000000000000004 | 5.5 | 8 | 10 | 12 | 15 | 18 | 25
Volume (in^3) | 48.5815 | 48.5815 | 58.2977 | 48.5815 | 43.7233 | 34.9786 | 29.1489 | 24.2907 | 24.2907
Power density [W/in^3] | 67.9272 | 90.5695 | 94.3433 | 164.6719 | 228.711 | 343.0665 | 514.5997 | 741.0235 | 1029.1994
State of Art Limit
  CoolGaNTM Transistors in BBUs DC/DC converters offer high power density of 1029 W/in3 at 25 kW BBU module power

## Slide 13: CoolGaNTM in monitor power SMPS
Si-based 200 W monitor power | Qisda 250W TV Power
SPEC | 90 – 264 VAC 20 Vout / 10 A
Topology | PFC + LLC
PCB layer | 2 layer 2Oz
Height | <24.5 mm
Case size | 220 x 155 x 24.5 mm
Power density | 3.9 W/inch³
GaN-based 250 W monitor power | Qisda 250W TV Power
SPEC | 90 - 264 VAC 19.5 Vout / 13 A
Topology | PFC + LLC
PCB layer | 2 Layer 2Oz
Height | <16 mm
Case size | 165 x 110 x 16 mm
Power density | 14.1 W/inch³
Chart: 
| 0.253 | 62.3 | 126.5 | 194.4 | 252.5
115Vac | 0.9141 | 0.9275 | 0.9444 | 0.9419 | 0.934
230Vac | 0.9177 | 0.9368 | 0.9569 | 0.9544 | 0.9498
Output power (W)
Efficiency
91.26%@ Si-Based 200W 115 VAC
2%+ Efficiency improvement with CoolGaNTM
System level optimization with CoolGaNTM increases power density nearly 4x and efficiency up to 96%

## Slide 14: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 15: Reference board 1 kW fanless telecom SMPS
REF_1KW_PSU_5G_GaN
Features
Benefits
CCM totem pole PFC
HB LLC
Full digital control in both PFC and LLC
Fan-less design
Typ. telecom surge requirements fulfillment
Addressing the new requirements of outdoor edge computing SMPS
Innovative fan-less cooling concept demonstrator
Low profile
High efficiency
Power density: 2 x 500 W PSU version (same form factor as 500 W PSU)
Technical details
Input voltage | Nom. 100 - 250 VAC; Max 85 - 305 VAC
Output voltage | 12 V
Output current | 83 A
Output power | 1000 W
Efficiency | ≥ 96% peak
Height | 1U
Cooling | Natural convection
Ambient Temperature | -40 to 70° C
Board Status | Available (Sales Product Name REF_1KW_PSU_5G_GAN)
Learn More | 
Infineon components | CoolGaNTM 600 V G1 (IGT60R070D1) CoolMOSTM S7 600 V (IPT60R022S7) and CFD7 (IPT60R055CFD7) OptiMOSTM 40 V (BSC009N04LSSC), all in SMD packages top side cooling
Just as example of outdoor edge server
Visit web page

## Slide 16: Reference board 3.3 kW server SMPS - High frequency and high density
 | Technical details
Input voltage range | 180 VAC ~ 275 VAC
Output voltage range | 51 - 48 VDC
Output power maximum | 3300 W
Efficiency target | ~97.5 % (without fan)
Power factor (load > 10%) | PF > 0.95 @ 180 ~ 275 VAC iTHD < 10 % @ 180 ~ 275 VAC
Ambient temperature | 0 °C to 50 °C
LLC Resonant frequency | 530 kHz
Board Status | Available (Sales Product Name- REF_3K3W_HFHD_PSU)
Learn More | 
Infineon components | CoolGaNTM Transistor 600 V G5 (IGT60R042D2) CoolSiC™ MOSFET 650 V (IMT65R057M1H) CoolMOSTM 600 V (IPT60R022S7, IPT60R016CM8NEW) CoolSiC™ Schottky diode 650 V (IDL10G65C5) EiceDRIVER™ (2EDB9259Y, 1EDN8511B, 1EDN8550B, 1EDB8275F) OptiMOS™ 5 (IQE046N08LM5) CoolMOS™ 800 V (ICE2QR2280G) Schottky diode (BAT46WJ, BAT165) MOSFET 60 V (BSS138N) OPTIREGTM Switcher (TLS4120D0EPV33) Digital isolator (4DIR1400H) Controller (XMC4200-Q48K256 for PFC, 3rd Party dsPIC33CK256MP203 for LLC)
Features
Benefits
Full Infineon‘s semiconductor solution
Complete power supply unit (PSU) including PFC + DC/DC
High efficiency, custom and in-house design integrated magnetics
Hold up time extension circuit
Benchmark 97.4% of efficiency: ~96 W/in³ in 1U form-factor
Highest efficiency & power density with CoolMOS™, CoolSiC ™, CoolGaN™
Custom integrated planar magnetic construction
Full digital control (PFC and DC/DC)
Totem-pole SiC PFC + Half-bridge GaN LLC
TR
Interleaved totem-pole PFC 2 x 65 kHz
Half bridge LLC 450 kHz-1.5 Mhz
Hold-up time extension circuit
REF_3K3W_HFHD_PSU
192 mm
40 mm
Visit web page
72 mm
GaN

## Slide 17: Reference board 8 kW server SMPS
REF_8KW_HFHD_PSU
Features
Benefits
Highest efficiency & power density with CoolMOSTM 8, CoolSiCTM , CoolGaNTM
Novel integrated planar magnetic construction
Full digital control (PFC and DC/DC)
Interleaved totem-pole PFC + Full-bridge GaN LLC
98% peak efficiency
Power density 113 W/in³ (-38% volume vs ORv3 specification)
Hold up time extension circuit for 20 ms @100% Load
400 kHz LLC switching frequency enabled with GaN
446mm
73.5mm
40mm
1-ph AI PSU 8 kW
73.5 x 720 x 40 mm
Learn more | 
Infineon components | CoolGaNTM Transistor 650 V G5 (IGT65R035D2) CoolSiC™ MOSFET 650 V (IMT65R040M2H, IMT65R015M2H) CoolMOSTM 600 V ( IPT60R016CM8, IPT60R050G7) CoolSiC™ Schottky diode 650 V (IDL12G65C5) OptiMOS™ 5 (IQE03xN08LM6) OptiMOS™ 80 V (ISC018N08NM6) EiceDRIVER™ (1EDB8275F, 1EDN8511B, 2EDB9259Y, 1EDN8550B) Schottky diode (BAT46WJ, BAT165) MOSFET 60 V (BSS138N) CoolMOS™ 800 V (ICE2QR2280G) OPTIREGTM Switcher (TLS4120D0EPV33) Digital isolator ( 4DIR1400H) Controller (XMC4200 for PFC, 3rd party MCU for LLC) (components could be a subject to change)
Technical details | 
Input voltage range | 180 VAC ~ 275 VAC
Output voltage | 50 VDC nominal
Output current | 160 A
Output power max | 8000 W
Efficiency | ~ 98%
Power factor (load > 10%) | PF > 0.98, 20%80% load iTHD < 10%, 20%80% load
Temperature Ambient | 0°C to 40°C
Visit web page

## Slide 18: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 19: System-level key takeaways
CoolGaN™ has best FOMs and lowest RDS(on) to enable new topologies and higher switching frequency
Totem pole PFC higher efficiency enabled by CoolGaN™
LLC higher frequency and density enabled by CoolGaN™
CoolGaN™ enables natural convection cooling SMPS (fan less)
SMPS in various applications is trending towards higher power, density and efficiency
A broad portfolio of CoolGaN™ Transistors, drivers, BDS, and system evaluation boards are available and in development to meet application requirements and accelerate customers’ designs

## Slide 20: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42
Notes: Slide for Moderator

## Slide 21: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 22: CoolGaN™ Transistor 650 V G5 for highly efficient power conversion in SMPS applications
enabling high-frequency operation & increased power density
CoolGaN™ targets consumer & industrial applications

## Slide 23: CoolGaN™ Transistor 650 V G5 with best-in-class FOMs Highest efficiency at increased switching frequencies between technologies
​
​
​
​
Qoss x RDS(on) typ. [nC x mΩ]
Eoss x RDS(on) typ. [µJ x mΩ]
Enables better soft-switching performance (e.g., LLC), and reduction of passives, thus increased power density
Enables lowest switching losses in hard-switching topologies (e.g., classic boost PFC, inverters)
Enables usage in topologies with repetitive commutation (e.g. CCM totem pole PFC, bidirectional switching)
CoolGaN™ with outstanding FOM supports highly efficient fast switching operation & enables lowest switching and reduced driving losses
 | Voltage | RDS(on)*Eoss | RDS(on)*Qg | RDS(on)*Qoss | RDS(on)*Qrr
Silicon | 600 | 100% | 100% | 100% | 100%
SiC | 650 | 88% | 44% | 13% | 9%
GaN | 650 | 91% | 11% | 11% | 0%
Qg x RDS(on) typ. [nC x mΩ]
Enables reduced driving losses, especially at light-load conditions
Allows to reach higher efficiency at increased frequency
Qrr x RDS(on) typ. [nC x mΩ]
GaN for highest power density
Chart: 
| IGT65R035D2 | SiC | Si
Eoss | 297.5 | 290.4 | 328.6
Chart: 
| IGT65R035D2 | SiC | Si
Qg | 269.5 | 1089 | 2449
Chart: 
| IGT65R035D2 | SiC | Si
Qoss | 1995 | 2244 | 17701
Chart: 
| IGT65R035D2 | SiC | Si
Qg | 0 | 524 | 6107

## Slide 24: CoolGaN™ Transistor 650 V G5 with best-in-class FOMs Highest efficiency at increased switching frequencies between competition
​
​
​
CoolGaN™ Transistor 650 V G5 with best-in-class Qg
Enables reduced driving losses, especially at light-load conditions
Qg x RDS(on) typ. [nC x mΩ]
CoolGaN™ Transistor 650 V G5 with best-in-class Qoss
Enables better soft-switching performance (e.g., LLC), and reduction of passives, thus increased power density
CoolGaN™ Transistor 650 V G5 with best-in-class Eoss
Enabling lowest switching losses in hard-switching topologies (e.g., classic boost PFC, inverters)
Qoss x RDS(on) typ. [nC x mΩ]
Eoss x RDS(on) typ. [µJ x mΩ]
CoolGaN™ to reach higher efficiency at increased frequencies, supporting size reduction and power density
CoolGaNTM.
650 V G5
CoolGaNTM
600 V G1
Chart: 
| IGLR65R140D2 | IGLR60R190D1 | Competitor I | Competitor T
Qg | 266 | 448 | 386.4 | 735
Chart: 
| IGLR65R140D2 | IGLR60R190D1 | Competitor I | Competitor N | Competitor T
Qoss | 1960 | 2240 | 3381 | 3240 | 5250
Chart: 
| IGLR65R140D2 | IGLR60R190D1 | Competitor I | Competitor N | Competitor T
Eoss | 280 | 350 | 496.8 | 384 | 585
CoolGaNTM.
650 V G5
CoolGaNTM
600 V G1
CoolGaNTM.
650 V G5
CoolGaNTM
600 V G1

## Slide 25: CoolGaN™ Transistor 650 V G5 with best-in-class FOMs base line for high efficiency at increased switching frequencies
Chart: RDS(on) [mΩ]
| IGLD65R140D2 | IGLD60R190D1 | Competitor I | Competior N
Static RDS(on) max @ 25°C [mΩ] | 170 | 190 | 140 | 180
Thermal Drift [mΩ] | 49 | 54 | 49 | 66
Dynamic Drift [mΩ] | 1 | 23 | 35 | 48
Normalized RDS(on),dyn | 1.0046 | 1.0943 | 1.1852 | 1.1951
​
CoolGaN™ Transistor 650 V G5 with best-in-class Id_pulse rating
Allowing wide range input voltages in PFC topologies for design flexibility
Robustness against line drop events ensuring stable operation
ID pulse @ 125°C
Dynamic & thermal RDS(on) comparison
Tc =85°C, hard switching operation after 15 mins
CoolGaN™ Transistor 650 V G5 offer smaller dynamic 49 mΩ & thermal drift of RDS(on) over competition
CoolGaN™ offers ~ 20 % lower dynamic RDS(on) drift compared to competition
Enabling reduced conduction losses & better thermals
Chart: 
| IGLR65R140D2 | IGLR60R190D1 | Competitor I
Stack 1 | 14 | 11 | 11.5
CoolGaNTM.
650 V G5
CoolGaNTM
600 V G1

## Slide 26: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 27: 3.4 kW CCM totem-pole PFC evaluation board CoolGaN™ Transistor 650 V G5 offers better application performance than previous CoolGaN™ generations
CoolGaN™ Transistor 650 V G5 performance is better than previous CoolGaN™ generations
CoolGaN™ Transistor 650 V G5 drop-in replacement for previous CoolGaN™ generations and plug & play conversion of existing designs
CoolGaN™ Transistor 650 V G5 offers better performance over competition
Efficiency comparison at highline
DUT adapter board
Chart: Power [W]
| 398 | 793.88 | 1190.1099999999999 | 1586.04 | 1983.99 | 2378.83 | 2774.9 | 3170.45 | 3566.86
IGOT60R042D1 | 98.4539 | 98.99 | 99.1164 | 99.0514 | 98.9625 | 98.8954 | 98.8399 | 98.7691 | 98.5713
IGOT65R035D2 | 98.3509 | 99.0887 | 99.1808 | 99.1132 | 99.0555 | 99.0222 | 98.9094 | 98.8406 | 98.5713
Competitor T | 97.9398 | 98.5175 | 98.8068 | 98.9144 | 98.8706 | 98.8282 | 98.7685 | 98.7426 | 98.6116

## Slide 28: 3.2 kW server application, LLC application analysis CoolGaN™ 650 V G5 enables highest efficiency at increased switching frequencies
CoolGaN™ allows increased switching frequency keeping the same power loss
At 250 kHz and above CoolGaN™ offers similar efficiency as at 100 kHz operation
Further increase of power density due to 36 % reduction of resonant tank
Primary-side transistors |  |  |  |  | 
Items | VDS_max (V) | ID_cont (A) | RDS(on)_typ (mΩ) 25°C | Total Qg (nC) | Total Qrr (nC)
CoolGaN™ | 650 | 39 | 50 | 6.7 | 0
SiC | 650 | 36 | 60 | 46 | 142
Si MOSFET | 650 | 45 | 50 | 102 | 1200
Chart: Efficiency [%]
| 100kHz | 250kHz | 500kHz
100% load GaN | 0.98064 | 0.97998 | 0.97361
100% load SiC | 0.9807 | 0.97882 | 0.96858
100% load Si | 0.97877 | 0.97364 | 0.94121
250 kHz
Optimized!
Chart: ve(cm3)
| 100kHz | 250kHz | 500kHz
Transformer size | 41 | 32.6 | 25
Chart: ve(cm3)
| 100kHz | 250kHz | 500kHz
Capacitor size | 38.1 | 13.8 | 5.7
× 5
× 2
Size reduction
Component count reduction
Chart: Switching frequency
| 100kHz | 250kHz | 500kHz
Inductor | 1 | 1 | 1
Transformer | 1 | 0.79512 | 0.60976
Capacitor | 1 | 0.3622 | 0.14961
Combined | 1 | 0.64301 | 0.47162

## Slide 29: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
  31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 30: CoolGaN™ Transistor 650 V G5 portfolio - broad portfolio enabling optimized product selection
 | CoolGaN™ Transistors 650 V G5 |  |  |  |  |  |  | 
RDS(on, typ) [mΩ] | 650 V |  |  |  |  |  | 700 V | 
 | ThinPAK 5x6 | DFN 8x8 | DSO TSC | TOLL | TOLT | ThinPAK 8x8 | DPAK | ThinPAK 5x6
500 |  |  |  |  |  |  | IGD70R500D2S | 
270 | IGLR65R270D2 |  |  |  |  |  | IGD70R270D2S | IGLR70R270D2S
200 | IGLR65R200D2 |  |  |  |  |  | IGD70R200D2S | IGLR70R200D2S
140 | IGLR65R140D2 | IGLD65R140D2 |  | IGT65R140D2 |  | IGL65R140D2 | IGD70R140D2S | IGLR70R140D2S
110 |  | IGLD65R110D2 |  |  | IGLT65R110D2 | IGL65R110D2 |  | 
80 |  | IGLD65R080D2 |  |  |  | IGL65R080D2 |  | 
55 |  | IGLD65R055D2 | IGOT65R055D2 | IGT65R055D2 | IGLT65R055D2 | IGL65R055D2 |  | 
45 |  |  | IGOT65R045D2 | IGT65R045D2 | IGLT65R045D2 |  |  | 
35 |  |  | IGOT65R035D2 | IGT65R035D2 | IGLT65R035D2 |  |  | 
25 |  |  | IGOT65R025D2 | IGT65R025D2 | IGLT65R025D2 |  |  | 
17 |  |  |  | IGT65R017D2* | IGLT65R017D2* |  |  | 
ES timeline | Released |  |  | Q3 CY25 | Q3 CY25 | Available | Available | Available
QS timeline |  |  |  | Q1 CY26 | Q1 CY26 | Q3 CY25 | Q3 CY25 | Available
SOP |  |  |  | Q2 CY26 | Q2 CY26 | Q3 CY25 | Q3 CY25 | Q1CY25
Coming soon
Released
*timeline to be done
High Power SMPS
Medium Power SMPS

## Slide 31: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42
Notes: Slide for Moderator

## Slide 32: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 33: CoolGaN™ Transistor 100 V G3 & Si: FOM comparison
 | CoolGaN™ Transistor 100 V G3 | 100 V BiC Si
Package | RQFN 5x6, DSC | SuperSO8, BSC
RDS(ON),max | 1.4 mΩ | 2.24 mΩ
RDS(ON),typ | 1.1 mΩ | 1.8 mΩ
Qoss,typ | 94 nC | 135 nC
Qrr,typ | 0 nC | 70 nC
Qg,typ | 24 nC | 73 nC
CoolGaNTM offers 60% lower RDS(ON), 40% lower Qoss, 3x lower gate losses and Zero Qrr
CoolGaN™ Transistors Medium Voltage RQFN products set a new benchmark in power systems design
They offer a first for GaN routable QFN (RQFN) package form factor
Enables seamless integration into existing solutions
Reducing the need for substantial layout changes or the creation of new board designs

## Slide 34: Efficiency over IOUT at different switching frequencies VIN = 48V, VOUT = 12V
Chart: IOUT [A]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
GaN 48 V | 3.387 | 93.7278 | 96.4298 | 97.2571 | 97.8286 | 98.1163 | 98.268 | 98.3745 | 98.4204 | 98.4595 | 98.4787 | 98.4735 | 98.4598 | 98.4383 | 98.407 | 98.3748 | 98.3439 | 98.2919 | 98.2448 | 98.1907 | 98.1391 | 98.0755 | 98.0158 | 97.9436 | 97.881 | 97.7969 | 97.7278 | 97.6397 | 97.5629 | 97.4674 | 97.3851
SFET8 48 V | 1.1946 | 84.4809 | 91.7601 | 94.3202 | 95.6361 | 96.4039 | 96.8454 | 97.141 | 97.3593 | 97.5017 | 97.6189 | 97.6967 | 97.761 | 97.7904 | 97.8239 | 97.8271 | 97.8327 | 97.816 | 97.8086 | 97.7812 | 97.7585 | 97.7131 | 97.6868 | 97.6326 | 97.5885 | 97.5289 | 97.4759 | 97.411 | 97.3502 | 97.2805 | 97.2096
Chart: IOUT [A]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
GaN 48 V | 0.77929 | 77.8967 | 88.5721 | 92.5945 | 94.3576 | 95.261 | 95.7464 | 96.0811 | 96.2885 | 96.4651 | 96.556 | 96.6134 | 96.6517 | 96.6604 | 96.6811 | 96.6563 | 96.6279 | 96.5918 | 96.5511 | 96.4807 | 96.418 | 96.3414 | 96.2616 | 96.1585 | 96.0569 | 95.9508 | 95.8325 | 95.6843 | 95.5494 | 95.3703 | 95.2276
SFET8 48 V | 0.23017 | 52.0131 | 69.9356 | 78.8918 | 83.7674 | 86.8794 | 88.7505 | 90.11 | 90.9255 | 91.6324 | 92.096 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A
With Si:
fSW=200 kHz Big inductor!
CoolGaN™
Si FETs
CoolGaN™
Si FETs
With GaN
fSW=1 MHz
Smaller inductor!
Si FETs get too hot even at 10 A!!
Switching at higher frequencies allows the use of smaller and lower cost passive components for DC/DC applications
Si FETs get too hot at higher frequencies, while GaN run much cooler, and provide high efficiencies!
CoolGaNTM offers substantial advantages at higher frequencies 1 MHz compared to Silicon FETs

## Slide 35: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 36: LLC – ZVS (zero voltage switching) & parasitics
Equivalent switch node capacitance Csw:
  Primary Coss
  SR Coss
  SR reverse recovery charge (Si)
  Transformer parasitic capacitance
  Layout stray capacitance
  ZVS could only be ensured if Lm energy overcome Csw energy
SR switch capacitance is essential for primary zero voltage switching mechanism

## Slide 37: ZVS energy – GaN vs Si SR
Si SR
GaN SR
IGC033S101
GaN SR enables easier primary zero voltage switching than Si SR

## Slide 38: CoolGaN™ SR in LLC
(Qoss) Lower device charge ->
  Lower circulating current
  Less fringing flux due to lower Tx air gap
  Less dead-time needed
  Better control at no load
(Qg) Lower gate charge -> Lower gate-drive losses
(RDS(on)) Lower resistance per area -> Smaller package
(Qrr) Lack of reverse recovery– Allows above resonance
Reduced AC losses
Less dummy load
Less RMS losses
Reduced gate losses
Wider control range
GaN

## Slide 39: 6.5 mm TV SMPS evaluation board with CoolGaN™
Parameters | Values | Parameters | Values
Vin | 365 ‑ 405 VDC | Lr | 6 µH
Vout | 22 VDC | Cr | 4 x 4.7 nH
Fres | 500 kHz | Lm | 40 µH
N | 9:1:1 | Height | <6.5 mm
GaN SR is a high frequency SMPS enabler due to its superior properties

## Slide 40: Results - GaN vs Si SR
GaN SR
Si SR
Below resonance
Above resonance
Up to 0.3%
Qrr impact is here
Up to 0.6%
GaN SR perform better up to 0.3% below resonance and 0.6% above resonance than Si SR

## Slide 41: CoolGaN™ Transistors 100 V G3 value proposition in SMPS
GaN used as synchronous rectifier (SR) in LLC converter:
Facilitates voltage regulation at no load
Less dummy load -> Reduced stand-by losses
Enables above-resonance due to the absence of Qrr
Wider control frequency range -> LLC above resonance
Improves the converter efficiency
Reduced Rdson/Area -> Conduction losses improved
Reduced primary RMS current -> Lower ZVS energy
Reduced dead-time -> Faster switching times
Reduced fringing flux -> Lm can be increased
Reduced gate loss -> Lower gate charge -> Easy paralleling

## Slide 42: Agenda
SMPS application description and trends
1
  4
CoolGaN™ in current & next-generation SMPS applications
2
  8
System application boards
3
  14
System-level key takeaways
4
  18
High voltage CoolGaN™ (650 - 700 V)
5
  20
Technology overview & power device comparison
5.1
21
Value proposition of HV GaN in SMPS
5.2
26
Portfolio leadership
5.3
29
Medium voltage CoolGaN™ (60 - 200 V)
6
31
Technology overview & power device comparison
6.1
32
Value proposition of MV GaN in SMPS
6.2
35
Portfolio leadership
6.3
42

## Slide 43
 |  | BDS | CoolGaN™ Transistors G3 |  |  | GaN transistors |  | 
Voltage | RDS(on) (Typ @ 25C) | WLCSP | PQFN 3x3 BSC | PQFN 3x3 DSC | PQFN 3x5 BSC | PQFN 3x5 DSC | RQFN 5x6 DD | RQFN 3.3x3.3 SD
200V | 6.7 mΩ |  |  |  |  | * IGC090S20S11 |  | 
120V | 2.7 mΩ |  |  |  |  | IGC037S12S1* |  | 
100V | 16 mΩ |  |  |  |  |  |  | 
 | 9.4 mΩ |  | IGB110S101 | IGB110S10S1 |  |  |  | 
 | 5 mΩ |  |  | IGB070S10S1 * |  |  |  | 
 | 2.5 mΩ x2 |  |  |  |  |  |  | 
 | 2.4 mΩ |  |  |  | IGC033S101 | IGC033S10S1 |  | 
 | 1.1 mΩ |  |  |  |  |  | IGD015S10S1 | 
80V | 2.3 mΩ |  |  |  |  |  |  | IGE033S08S1
 | 1.8 mΩ |  |  |  |  | IGC025S08S1 |  | 
60V | 1.3 mΩ |  |  |  |  | IGC019S06S1 |  | 
40V | 9 mΩ | IGK012B041S2 |  |  |  |  |  | 
 | 6 mΩ | IGK080B041S |  |  |  |  |  | 
 | 4 mΩ | IGK048B041S |  |  |  |  |  | 
Please find below our preliminary timeline, for specific project: all dates are subject to change. |  |  |  |  |  |  |  | 
EES |  |  |  |  |  |  | Q1 CY25 | Q1 CY25
ES |  | available | available | available | available | Available |  | 
QS |  | Q2 CY25 | productive | productive | productive | Q1 CY25 | Q3 CY25 | Q3 CY25
CoolGaNTM 40 – 200 V G3 wide range of transistors and bidirectional switches portfolio
Released
In development
1QS Q1 CY25
2 SOP: Q1 CY25

## Slide 44: CoolGaN™ Transistors 60 - 200 V G3 in 3x5, 3x3 PQFN
CoolGaN™ Transistors 60 - 200 V G3
Features
PQFN
Portfolio
ES1 | Available
SOP2 | Q1’25
Enhancement mode transistor – Normally OFF switch
No reverse-recovery charge
Capable of reverse conduction
Low gate charge, low output charge
Superior commutation ruggedness
Tj = -40°C – 150°C
RthJA 1 layer PCB= 60 °C/W
RthJC Top = 0.5 °C/W
RthJC bottom = 1.9 °C/W
Cost-performance optimized 3x5 PQFN package
Available in BSC and DSC easy to assemble PQFN package
Full system enablement with top cooling
Highest efficiency with low switching losses
Improved power density and overall system cost
Benefits
 | Sales Code | Package
EiceDRIVER™ HB 120V 2EDL50X3U2D* | 2EDL5013U2D | TSNP-12 2x2
EiceDRIVER™ 1EDN71x6x 1CH driver family | 1EDN71x6x | PG-TSNP-7, VSON-10
Digital power controller for 48V DC/DC applications | XDPP11xx | PQFN24, PQFN40
Connected products
Final DS available
*for specific applications
Voltage | RDS(on) typ. | Package | Sales Code
60 V | 1.3mΩ | 3x5 PQFN DSC | IGC019S06S1
80 V | 1.8mΩ | 3x5 PQFN DSC | IGC025S08S1
100 V | 2.4mΩ | 3x5 PQFN BSC | IGC033S101
100 V | 2.4mΩ | 3x5 PQFN DSC | IGC033S10S1
120 V | 2.7mΩ | 3x5 PQFN DSC | IGC037S12S1
100 V | 5mΩ | 3x3 PQFN DSC | IGB070S10S1
200 V | 6.7mΩ | 3x5 PQFN DSC | IGC090S20S1
100 V | 9.4mΩ | 3x3 PQFN BSC | IGB110S101
100 V | 9.4mΩ | 3x3 PQFN DSC | IGB110S10S1
1Engineering Samples, 2Start of Production

## Slide 45: CoolGaN™ Transistors 80 - 100 V G3 in 3.3x3.3 SD, 5x6 RQFN
CoolGaN™ Transistors 80 - 100 V G3
Features
RQFN
Portfolio
GaN Transistors 80 – 100 V G3 in Si-footprint packages!
Enhancement mode transistor – normally OFF switch
No reverse-recovery charge
Capable of reverse conduction
Low gate charge, low output charge
Superior commutation ruggedness
Tj = -40°C – 150°C
Best thermal solution in small footprint
Available in DSC easy to assemble RQFN package
Full system enablement with top side cooling
Highest efficiency with low switching losses
Improved power density and overall system cost
Benefits
 | Sales Code | Package
EiceDRIVER™ HB 120V 2EDL50X3U2D* | 2EDL5013U2D | TSNP-12 2x2
EiceDRIVER™ 1EDN71x6x 1CH driver family | 1EDN71x6x | PG-TSNP-7, VSON-10
Digital power controller for 48V DC/DC applications | XDPP11xx | PQFN24, PQFN40
Connected products
Target DS available
*for specific applications
Voltage | RDS(on) typ. | Package | Sales Code
80 V | 2.3mΩ | 3.3x3.3 RQFN DSC | IGE033S08S1
100 V | 1.1mΩ | 5x6 RQFN DSC | IGD015S10S1
EES1 | Q1’25
SOP2 | Q3’25
1Early Engineering Samples, 2Start of Production

## Slide 46: Infineon is your reliable partner with GaN solutions!
Reliability
Density
System solution
Trusted supplier
Notes: Slide for Moderator

## Slide 47
Notes: Slide for Moderator